## Slide 1: Introduction to GIS Short Course
April 27th and 28th, 2017

## Slide 2: My Background
Not in GIS!
Environmental Science at Acadia
Environmental Scientist/Project Coordinator at GeoGrid Environmental
M.Sc. Geology at Acadia
Use Geographic Information Systems in all 3
Applied, Pragmatic approach to GIS

## Slide 4
Elevation contours and water table contours of a spill site in Wimborne, Alberta

## Slide 5
Excavated View
1989 View
Final Contour
Cut and fill diagram of a site in Elk Point, Alberta

## Slide 6
Cut and fill diagram of a site in Elk Point, Alberta

## Slide 11: What is Geographic Information?
GIS = Geographic Information System(s)
Geographic Information is any information with a location associated with it (so, everything)
Any information you can put on a map
(and want to)

## Slide 12
Standard NTS Topographic Map

## Slide 13: Why do we bother?
Often a map is the best way to present and analyze information with a geographic component.
Maps allow us to view multiple types of information together (“layers”) to make connections.

## Slide 14: Introduction to GIS Short Course
Day 1: How do you make a map in QGIS?
  Add data to the map
  Format the data to look pretty
  Export/Print the map
  Getting your data into QGIS

## Slide 15: Introduction to GIS Short Course
Day 2: Creating, importing, and manipulating GIS Data
  Make a map of your study sites
  Create and edit data in QGIS
  Interpolation and contouring (Raster processing)
  Vector data analysis
  Going over participant projects

## Slide 16: Assignments
During each module you will:
  Create a QGIS Project
  Create a PDF of the map you made in that module
  Save the QGIS Project (and any data you generate during that module) in the correct folder.
You “must” complete these tasks!

## Slide 17: GIS Applications
GIS = Programs that work with geographic data
Google Earth (free to $400/year)
ESRI ArcGIS ($1500 base license, $4000 per extension; free basic versions available)
GRASS, QGIS (“free” or by donation)
MapInfo ($1995)
Whitebox GIS (also free)

## Slide 18: GIS Applications
All have same set of features:
  Basemaps
  Ability to add/edit/view geographic data (some free versions don’t allow editing)
  Analysis Tools
We will be using QGIS because:
  It doesn’t cost money to install
  It works (and works well) on multiple platforms
  There is no license restriction (you can use it forever)

## Slide 19: How is GIS Data Organized?
GIS Data is organized in layers
Each layer contains similar data that is usually displayed in a similar way.
Layers

## Slide 20: Types of Layers
Raster Layers
  Contain a grid of data with a data value in each square
  Can be color data (like a picture)
  Can be other data (like elevation, concentration)
Vector Layers
  Contain a collection of points OR lines OR polygons (“features”)
  Also contain data about these features (Sample number, elevation, depth, strike, dip; known as “attributes”).
The power of GIS if often in comparing layers with each other and examining relationships.

## Slide 21: Raster Layers
Can be displayed in a variety of ways – “color ramp” (shown below), grayscale, several discrete colors.
For any point on the map, you can obtain a value from a raster.
Also called a “surface”

## Slide 22: Vector Layers
Made up of one or more “features” that have “attributes”
Point OR line OR polygon features in a single layer

## Slide 23: Vector Data
Points
Lines
Polygons
Features, Fields, Attributes

## Slide 24: How could the following data be represented?
Soil conductivity (Points, Contours)
Water table depth (Points, Contours)
Sample locations (Points)
Strike & dip (Points, Contours)
Slope steepness & direction of slope (Points, Contours)
Roads (Lines, Polygons)
Habitat suitability (Polygons)
Bedrock type (Polygons)

## Slide 25
Identify the “layers” present, and their types

## Slide 26
Identify the “layers” present, and their types

## Slide 27: Exercise!

## Slide 28: Coordinate Reference Systems

## Slide 29: Coordinate Reference Systems (CRS)
GIS Data (raster and vector) is represented by coordinates (X and Y).
These X and Y coordinates can mean any number of things!
  Latitude, Longitude, UTM Easting, UTM Northing, Arbitrary XY data from a defined grid
Every GIS data file has a CRS, because X and Y coordinates must be represented somehow.

## Slide 30: Projections (“Project CRS”)
Earth is a sphere (actually, an ellipsoid), so to represent it on something flat (your screen, a piece of paper) we need a projection.
Projections are never perfect, always distort some combination of shape (angles), scale (distance), and area.
Mathematically, projections convert Latitude/Longitude values (angles) to X/Y values (distances).

## Slide 31: Mercator Projection
X
Y

## Slide 32: Transverse Mercator Projection
Low distortion for a very specific strip of the world
Used for local data
X
Y

## Slide 33: Universal Transverse Mercator Zones

## Slide 34: Conic Projection
X
Y

## Slide 35: Projections
Earth’s Surface (Latitude, Longitude)
Map Coordinates (in distance units)
Projection
Coordinate Reference Systems
The XY coordinates of a particular dataset
Can be lat/lon (positions on the earth’s surface) or map coordinates (that can be related to lat/lon using a projection)

## Slide 36: Projections/CRSs
Dataset (layer you add to QGIS)
The map you look at
Layer CRS/Projection
Project CRS/Projection
Dataset (layer you add to QGIS)
Layer CRS/Projection

## Slide 37: Projections/CRSs
The CRS for a dataset can be projected (XY values in distance units) or geographic (latitude/longitude)
The projection in which you view geographic data can be different than the CRS of the dataset (“on-the-fly projection”)
If your data is not plotting in the right place, you have a CRS problem!

## Slide 38: Common CRSs
WGS84 = Latitude/Longitude
NAD83 = Latitude/Longitude fixed for North American Plate
Nova Scotia is UTM Zone 20N
For small areas (less than 50-100 km across) use UTM!
For large areas (between UTM zones) use World Mercator or Albers Equal Area Conic
For the arctic, you may need to use other projections

## Slide 39: Exercise!

## Slide 40: Introduction to GIS Short Course
January 16th & 17th, 2016

## Slide 41: What is Geographic Information?
GIS = Geographic Information System(s)
Geographic Information is any information with a location associated with it (so, everything)
Any information you can put on a map
(and want to)

## Slide 42: Vector Data
Points
Lines
Polygons
Features, Fields, Attributes

## Slide 43: Raster Layers
Can be displayed in a variety of ways – “color ramp” (shown below), grayscale, several discrete colors.
For any point on the map, you can obtain a value from a raster.
Also called a “surface”

## Slide 44: Projections
Earth’s Surface (Latitude, Longitude)
Map Coordinates (in distance units)
Projection
Coordinate Reference Systems
The XY coordinates of a particular dataset
Can be lat/lon (positions on the earth’s surface) or map coordinates (that can be related to lat/lon using a projection)

## Slide 45: Projections/CRSs
Dataset (layer you add to QGIS)
The map you look at
Layer CRS/Projection
Project CRS/Projection
Dataset (layer you add to QGIS)
Layer CRS/Projection

## Slide 46: What Happened in Day 1
Adding data into QGIS
Zoom, pan, navigate around the map
Changing the layer style (raster and vector)
Export your map using the print composer

## Slide 47: Making A Map
Prepare your data
Add your data
Make sure your data is in the right place (ensure correct CRS) and pick a Project CRS
Change the style of your layers
Export your map using a print composer (add north arrow and scale bar)

## Slide 48: Outline for Day 2
Refresher
Make a map of Study Sites in Nova Scotia
Creating and Editing Vector Layers
Introduction to Raster Processing
  Interpolation & contouring
Introduction to Vector Processing
  Selecting vector data, manipulating vector data
Your questions/projects!